8x8 LED Matrix Pattern
Description: - In this project we are using max7219 IC, this is display driver ic which works on SPI communication protocol. 8x8 LED matrix is two dimensional LED array which make a LED screen which can be used to display message and pattern or information on it. Our TV and phone screen also works on same mechanism as 8x8 LED matrix display ic max7219.
Components required:
In this project we are using Arduino board which will interface with 8x8 LED matrix with help of max7219 driver IC, so we will require components which are described below.
Components:
- Arduino board
- Arduino software
- 8x8 led matrix board with max7219 IC
- Jumper wire(M-F: 5)
Library:
Led Control library.
Connections:
Arduino board interfacing with 8x8 LED matrix board will be done with male to female jumper wire and connection for this project is shown below.
Connection to make:
S no.	LED matrix Pin	Arduino Pins
1.	VCC	+5v Pin
2.	GND	Ground Pin
3.	CS	D10
4.	CLK	D11
5.	Din(MISO)	D12

Follow the following Steps to make this project: -
STEP1: -Install the Arduino software
STEP2: -PROGRAMMING
follow the given code
STEP3: - Add these libraries to your arduino IDE using below steps: -
Unzip the downloaded library and copy extracted folder.
Now go to Arduino Installation directory
Then go to libraries folder and paste your copied folder into it.
Result:
If you have done every step correctly, then you can see different patterns on you LED matrix screen and you can also make many kind of animation face and pattern on you LED screen.