Alarm System With Capacitive Touch
Description- This Project is interfacing of a capacitive sensor with the Arduino and raise an alarm whenever any person touched on it.
Components required- In this project we would requires the component and tools which are described below.
- Arduino board
- Touch sensor
- Led(1)
- Resistor(1)
- Buzzer
- Jumper wire(M-M: 2 and M-F: 5)
- Arduino Software (IDE)
- Bread board
Connection: - In this project we would connect Arduino board with the capacitive touch sensor and buzzer alarm to detect rather the sensor is touched or not and according to that output can be seen on the hardware and the software.
Table of connection: -
S no.	Components Pin	Arduino Pins
1	Capacitive sensor VCC	5.v supply.
2.	Capacitive sensor GND	GND
3.	Capacitive sensor output	D4 pin
4.	Green Led.	D13 pin
5	Buzzer	D3 pin.

Follow the following steps to perform this project: -
STEP1: -Install the Arduino software
STEP2: -PROGRAMMING
Follow The given code
Step3: - Check if the board and port are selected correctly in arduino IDE tools menu.
Step 4: - Uploading the program to Arduino board by clicking on the upload button which is shown in the picture below. And check the result of you project.
After the code uploading you can check the result in the Arduino Serial monitor and our hardware also.
Result:
If you have done every step correctly, then you can see the output on both the serial monitor and the hardware.
This project is based on the capacitive touch sensor which is same as our android touch screen phone’s screen.
A capacitive touch sensor is a sensor which creates a capacitor with plate and skin of person who touch it. And our Arduino read’s that value from any digital pin of Arduino board and convert that capacitance into a digital value. Whenever someone touches a sensor than it gives a low out which can be read at serial monitor Arduino board.