Alarm System With Sound Sensor
Description: - In this project we will use sound detector sensor and make alarm system which will detect any sound in the room or any kind of noise disturbance, by beeping up the buzzer. And also we would able to see the result on the Serial monitor of Arduino Software (IDE).
Component & tools required: - In this project we would require the component and tools which are described below.
Arduino Uno
Breadboard
Sound sensor module
Led (2)
Resistance (220 ohm) -- 2
Buzzer
Jumper wires(M-F: 5 and M-M: 3)
Arduino IDE
Connection: - In this project we will connect an Arduino board with the sound sensor module to detect the noise and output is generated by raising the alarm with the help of buzzer.
Table of connection: -
S no.	Components Pin	Arduino Pins
1	Sound sensor VCC	5.v supply.
2.	Sound sensor GND	GND
3.	Sound sensor output	A2 pin
4.	Red Led	D3 pin
5.	Green Led.	D2 pin
6	Buzzer	D5 pin.

Follow below Steps to make this project: -
STEP1: -Install the Arduino software
STEP2: -PROGRAMMING
Follow the given code
Step3: - Check if the board and port are selected correctly in Arduino IDE tools menu.
Result: - if you have done everything correctly than you would have same results which are shown below.
When the sounder sensor does not hear any noise than buzzer remain silent and Green is off, this means that Alarm is off. This result can be seen of Hardware and software both.
When the sound sensor detects the noise in environment then output voltage of it get dropped and Alarm get on. In this condition Red Led get turn on and buzzer start to buzzing a high pitch noise to detect the alarm.