Flex Sensor With Servo
Description: - In this project we are using our flex sensor to control the rotation of a servo motor. This type of mechanism is also used in the robotic hands robot.
Component required:- Here we are interfacing our flex sensor with servo motor and controlling the rotation of it with Arduino board according to the analog output of flex sensor.
So below described component will be needed in this project.
- Arduino Uno
- Flex sensor
- Bread board
- Servo motor
- Jumper wires (M-M: 7)
- Arduino IDE
Resistance(10k) -1
Connections: - Here we would connect our all component together. Please follow the below connection as shown.
Connection table:
S no.	Components	Arduino Pins
1.	Servo input	D5
2.	Servo Ground	GND
3.	Flex sensor Output	A0 Pin
4.	Servo motor supply	+5v

Follow the below steps to make your project:
STEP1: -Install the Arduino software
STEP2: -PROGRAMMING
follow the given code
Step3: - Check if the board and port are selected correctly in Arduino IDE tools menu.
Result:- If you have made everything correctly then you would also have result have shown below. In this project we are controlling reactionary motion of servo motor according to the bending in the flex sensor.
When flex sensor is getting bend in the positive direction then analog output voltage get increased and we can see our led starts glowing bright and also servo rotate in wide angle.
A flex sensor is analog sensor which output voltage changes according to the bending motion in that sensor. This kind of sensor is used to find strain in a beam or object.
And also vice versa happened when Flex sensor is bend in negative direction when analog voltage gets dropped down.
All these result also can be seen on the serial monitor of Arduino software in serial monitor.