Joystick Game With LEDs Pattern

Description: - In this project we are interfacing Game joystick with Arduino and make small LED game. According to movement of gaming joy stick, LED will glow and we would see the result of that movement on the serial monitor of Arduino IDE.
Component required: - In this project we are using a gaming joystick to make a LEDs game thus we would require this below described component in this project.
Arduino Uno
- Joystick module
- LED (4)
Resistors (220 ohm ) - 4
Jumper wires (M-M: 6, M-F: 5)
Breadboard
Connections: - We are now going to connect our Arduino with Analog joystick and other component so do connections which are shown below.
Connections Table: -
S no.	Components Pins	Arduino Pins
1.	Analog joystick VCC pin	+5v
2.	Analog joystick GND pin	GND
3.	Analog joystick button pin	7
4.	Analog joystick X pin	A0
5.	Analog joystick Y pin	A1
6.	Red led	8
7.	Green led	9
8.	Yellow	10
9.	White	11

Follow the below Steps to make this
STEP1: -Install the Arduino software
STEP2: -PROGRAMMING
Follow the given code
Step3: -Check if the board and port are selected correctly in arduino IDE tools menu.
Result: -In this project we are using gaming analog joystick and main purpose of this project to understand the working of gaming joy stick so we can use this for different purpose in future projects.
In this project we the movement of the joystick is getting change than according to that output on serial monitor and LEDs are changing.