Messaging Using RF Module
Description:- In this tutorial we are making a project which would transmit a message which is written in the serial monitor of Arduino serial monitor would be transfer through RF transmitter and then entered message can be seen on the LCD of receiver side of RF receiver.
Component required:-
- Two Arduino board
- Arduino software (IDE)
- One RF module
- LCD 16x2
- Male to female Jumper wire
- Bread board
- 10k potentiometer

Connection:- To make this project first we need to gather all the component described above and make connect as shown below.
Connection on transmitter side:-
On the transmitter side there would be an Arduino with RF module transmitter. By which message would be transmitted.
Connection table: -
S no.	RF transmitter	Arduino board pin
1.	VCC pin	+5v.
2.	Ground pin	Ground.
3.	Data pin	D12 Pin

Connection on receiver side:-
On the receiver side we would have a RF receiver module connected with the Arduino board and on LCD will be there for showing up the message on the LCD.
Connection table: -
S no.	Components	Arduino Pins
1.	RF VCC pin	+5v
2.	GND	Ground Pin.
3.	DATA	D11
4.	LCD VCC	+5
5.	LCD GND	Ground
6.	RS	D7
7.	EN	D6
8.	RW	Ground.
9.	Data D4 to D7 pin	Digital pin D5 to D2

Note: - Don’t forget to connect the variable resistor between pin 1 and 3 of LCD for controlling the brightness. and set the potentiometer till the brightness of the lcd become visible.
Follow below steps to make project: -
Step_1:follow the given code

Add requied libraries to your arduino IDE using below steps: -
Unzip the downloaded library and copy extracted folder.
Now go to Arduino Installation directory
Then go to libraries folder and paste your copied folder into it.
Step_2: Check the correct Arduino board and port in tool menu.
Step_3: Compile and Upload the code on both the Arduino by clicking on upload button.

Result: -
In our project we have two Arduino board in which one would be connected to your laptop and we would be place anywhere in range of 0 to 20 meter. And then you can start giving the message or data in serial monitor of Arduino software.
Transmitter side: - This part of our project would be get connect with our laptop because it would have serial data from Serial monitor of Arduino Software.
Receiver side: -
This part is receiver part which can be place anywhere in range of 0 to20 meter and all the message data sends from Serial monitor of Arduino from transmitter would be received here on LCD display.