4x4 Keypad Lock System
Description:-A 4x4 keypad locker is lock which only can be open with its correct password combination otherwise it won’t open. This project can be used in many different projects like automatic safe, keypad door lock system and other thing where keypad can be implemented.
Components required: - 4x4 keypad and servo lock is based on Arduino board thus programming for this code would be in Arduino software (IDE). And we will need below described component to make this project.
 Hardware: -
- Arduino Uno
- Mini breadboard
- Jumper wires (M-M: 14)
- Led (1 green and 1 red)
- Mini servo motor
- 4x4 keypad matrix
- Resister ( 2 ) 220ohm
Software: -
- Arduino IDE (1.6.4 or higher)
- Servo library
- Keypad library
Circuit: -

Connection table: -
S no.	Components pins	Arduino Pins
1.	Keypad R1 to R4	D8,D7,D6,D9
2	Keypad C1 to C4	D5,D4,D3,D2
3	Servo VCC	+5v
4	Servo GND	ground
5	Servo Input pin	D11
6	Green LED	D13
7	Red LED	D12

Follow the below following steps to make this project: -
STEP1: - Install the Arduino software and add the zip library of servo(if not present ) also add the keypad library.
download the required libraries :-
servo library
keypad and library
Add these libraries to your arduino IDE using below steps: -
- Unzip the downloaded library and copy extracted folder.
- Now go to Arduino Installation directory
- Then go to libraries folder and paste your copied folder into it.
STEP2: -  PROGRAMMING
Check The Given Code
Step3: - Check if the board and port are selected correctly in arduino ide tools menu.
Result: -In this project we are using the 4x4 keypad as locker system with Servo which would open the lock only when the password entered is correct.
Use correct password (here: '258') for opening of door and (# or * ) for closing the door.
If right pass key is pressed than it would light up the green led and open the lock and if you have entered a wrong pass then the Red led will continue to glow and won’t open the lock.
You can set up your password whatever you want and burn the code in the Arduino board again.
Access Accepted: - when you enter the correct pass key in the keypad then green led would light up and access through the lock would get  granted.
Project specifications: - This project can be used in many different places for different purpose. Like a door lock system, drawer or cubed lock and also as a safe lock system.
An automotive safe system can be made with help of GSM kit. To know the alarm if anyone tries to break a lock.